## Slide 1
This You Tube illustrates from start to finish
creation of some Bluetooth low energy functionality.
We use a Nordic Semiconductor nRF52832 ARM cortex MF4
Micro-controller and a DAP link USB com port and debug
interface and we develop code for it with the C++
Arduino / Genuino IDE
The hardware target is the RedBear BLE Nano - 2.
A tiny low cost very powerful little board !
Red Bear is now part of particle.io. They make
many kinds of these powerful little IOT devices.

## Slide 2
First you must setup the Arduino environment for the
RedBear BLE Nano-2 hardware.
You need to install the board support package for the
Red Bear BLE Nano - 2.
With some helpful instructions from Red Bear's github
site you can get this to work.
This is just a snippet of the steps, but they do work.

## Slide 3
Once you get it installed, it becomes one of the
hardware platform choices you can select when you
want to code a project “Arduino style”.
I selected "Examples for BLE_Nano2", sketch file:
"BLE_SimplePeripheral" as my example starting point.

## Slide 4
The goal for this project is to send date to
and receive data from my Android Lenovo / Moto G phone.
My modified Android sketch file 320 lines (with a lots of
pre-written system code backing it up) does everything
needed
I added a Write/Read back functionality sometimes called
"Loop Back" testing. This provides the demo I will
share with you on my cell phone.

## Slide 5
Now lets talk about the code.
The code sketch file is actually rather short
(But, let's not think about pre-written support code behind this !)
I really only had to modify or add about
6 lines of code, but I also added about
42 lines of comments to assist in my, and I hope,
your understanding.
On Line 22, I changed the name of device as it will appear
on my cell phone to add JMK - "That's Me"
I added some comments on Line 43-46 to clarify the jargon
A characteristic is some data that is sent over the wireless channel.
This data can be
1) Writeable by the cell phone (Cell phone sends to RedBear Nano)
2) Readable by the cell phone (RedBear Nano sends to cell phone upon request)
3) Notified to the cell phone (RedBear Nano sends to cell phone at intervals.)

## Slide 6
For my modifications a very important function was called
"gattServerWriteCallBack(..)"
This is an event handler (A.K.A - call back function)
that occurs when the BLE nano receives data from cell phone.
When that first kind of characteristic one that is writable
(referred to characteristic #1 in the program)
is written sent to the BLE Nano by the cell phone, this call back
is happens when the written data is received.
What I added are the two lines 184 and 185 that take this data and
use it to change also the Read characteristic (#2)
That way the user of the cell phone can latter request a
read back of this data to verify what was sent, was received.

## Slide 7
This is the callback function for the 1 second time task.
I Eliminated a repetitive call to the BLE Nano debug serial
port, at line 196, and added instead an LED blink at lines
213-214. This makes reading more important serial output
easier.
I also put in some comments pointing out how this 1 second
task updates the custom Notify characteristic #3
This 1 second task also updates (simulates) a changing heart
beat value for the heart rate update service On line 207.
Heart rate simulation is typical BLE sample code.

## Slide 8
The "loop()" is where non event related code gets put
to run any Arduino application.
For this demo sketch all the action happens in the
event related code.
So we just wait for events.

## Slide 9
Now lets talk about my test setup for Android G
phone.
For convenience and easy screen shot capture,
I remotely controlled my cell phone over a USB
cable with a free PC program called Visor.

## Slide 10
I used the free app "nrFConnect" provided by
Nordic Semiconductor to test their technology.
Read the friendly Nordic app manual if you can find it.
Or follow these steps in selecting the right buttons
and dials to see the things you need to see.
First you want to find the BLE device out there that
has our name "BLE_Periph_JMK" on it. Then
Press the Connect button.

## Slide 11
This opens up the list of our custom Characteristics.
Click on the Up arrow for the one with WRTE properties.

## Slide 12
Select date type "Text", type in "Joe",
make advanced select "Command"
Save as load choice "Joe1"

## Slide 13
Press Load, Click on Send

## Slide 14
So what happens ?
On your cell phone the WRITE Characteristic
Indicates "Joe" was written to the Nano.

## Slide 15
But how does the Cell phone user know that the
Nano got the data ?
We can find out by reading it back the READ
Characteristic from the Nano by clicking on the
down arrow as shown.
Once this is done the value "Joe" sent earlier now
appears as the value of the READ characteristic
Believe me this works for "Mike" as well.

## Slide 16
For more info and source code for the modified
Sketch, see my git hub site listed bottom of this
slide.
This breaks the ice for future BLE Adventures !